## Slide 1: Network size = number of hidden neurons
768 inputs
1 s sound picture,
24 pitches × 32 time steps
H hidden neurons
= the network size
Sheila
not Sheila
Sizes tested
8
16
32
48
64
80
95
95 = the most that fits in memory
3 training runs per size
results are the mean ± the spread
Everything else identical
same data, training and threshold rules
All 21 models run on the board
results identical to the Python reference
Notes: Here we changed one thing only: the number of hidden neurons, from 8 up to 95, the most that fits. Each size was trained three times; everything else stayed the same.

## Slide 2: Memory runs out at 95 neurons, time does not
Chart: hidden neurons
| 8 | 16 | 32 | 48 | 64 | 80 | 95
Memory (of 144 KiB) | 0.08355 | 0.1671 | 0.33507 | 0.5026 | 0.67014 | 0.83767 | 0.99474
Processing time (of 250 ms) | 0.02946 | 0.058984 | 0.11982 | 0.17954 | 0.2392 | 0.29899 | 0.35505
Limit | 1 | 1
1.5 KiB
memory per neuron
0.93 ms
processing time per neuron
95 neurons
memory full, time 35.5% used
Processing time: worst case on the board's RISC-V core (plain RV32IM firmware). Memory: the weights in the 144 KiB model area.
Notes: Each neuron costs one and a half kilobytes and almost a millisecond. At 95 neurons the memory is full, but processing uses only a third of the time per window: memory is the limit.

## Slide 3: Quality stops improving after 16 neurons
Chart: hidden neurons
| 8 | 16 | 32 | 48 | 64 | 80 | 95
F1 score, test clips | 0.69047 | 0.76447 | 0.75983 | 0.7898 | 0.76393 | 0.77453 | 0.78103
"Sheila" detected, live stream (2 of 3) | 0.511 | 0.61163 | 0.5975 | 0.6368 | 0.54407 | 0.6085 | 0.60537
69% → 76%
F1 score from 8 to 16 neurons
flat after 16
differences smaller than the spread of 3 training runs
Mean of 3 training runs per size; bars show ± 1 standard deviation. Live stream: 1 s windows every 250 ms; a detection needs 2 of 3.
Notes: Quality jumps from 8 to 16 neurons and then stays flat. Above 16, the differences between sizes are smaller than the spread between training runs.

## Slide 4: More neurons do not fix near misses
≈ 1/3
of near misses still pass,
at every size
Near misses sound like "Sheila": Sheena, shield, "shee" + another word.
One dense layer sees the whole second at once, not the order of the sounds.
→ needs a network that follows the order of sounds
Chart: hidden neurons
| 8 | 16 | 32 | 48 | 64 | 80 | 95
"shee" + another word | 0.39147 | 0.3721 | 0.3566 | 0.40507 | 0.32943 | 0.35467 | 0.34493
she-, sheet, shield, Sheena (computer voices) | 0.31043 | 0.3382 | 0.3028 | 0.3132 | 0.3153 | 0.28957 | 0.31947
another start + "eila" | 0.2922 | 0.33947 | 0.3045 | 0.34983 | 0.27367 | 0.33743 | 0.31277
"sh" alone | 0.007733 | 0.013567 | 0.0116 | 0.017467 | 0.009667 | 0.009667 | 0.009667
Accepted at the live threshold: per 1 s window (edited real recordings) or per word with "2 of 3" (computer voices). Mean of 3 runs.
Notes: A bigger network also does not reject near misses: about a third of words like Sheena or shield still pass, at every size. That needs a network that follows the order of sounds.

## Slide 5: 48 neurons match 95 with half the memory
48 neurons
efficient size
Memory
72 KiB (50.3%)
Processing time
45 ms
F1 score
79%
Live detection
64%
95 neurons
deployed now
Memory
143 KiB (99.5%)
Processing time
89 ms
F1 score
78%
Live detection
61%
48 has the best mean validation F1 (chosen before looking at test results); its quality differences to 95 are within the spread of 3 runs.
Notes: So 48 neurons give the same quality as 95 with half the memory and half the processing time: the efficient size for this design.

## Slide 6: Backup: how accuracy was measured
 | Network says "Sheila" | Network says "not Sheila"
Really "Sheila" 212 recordings | 160 found | 52 missed
Really another word 10,793 recordings | 37 false alarms | 10,756 correctly rejected
Deployed model (95 neurons) on the 11,005 test recordings, from speakers never heard in training
75.5%
Recall: "Sheila"s found
160 / 212
81.2%
Precision: right detections
160 / (160 + 37)
78.2%
F1: combines both
2 × P × R / (P + R)
Why not plain accuracy?
98% of the clips are not "Sheila": always answering "no" already scores 98.1%. Ours scores 99.2%, which hides the 52 misses.
Live detection (orange line)
Test clips in background noise, cut into 1 s windows every 250 ms; detected if "2 of 3" fires: 61% of "Sheila"s found, 0.3% of other words accepted.
Thresholds are chosen on separate validation recordings, never on the test set. The charts show the mean of 3 training runs; this table is the deployed run.
Notes: We measured accuracy with the F1 score on 11,005 test recordings from speakers the network never heard. F1 combines recall, how many real "Sheila"s it finds, and precision, how often a detection is actually right. We do not use plain accuracy: 98% of the clips are not "Sheila", so always saying "no" would already score 98%. The second line on the quality chart simulates the live demo: the share of real "Sheila"s that would light the LED.